## Slide 1
Measuring Slide Rule

## Slide 2
The Specimen
MS 1201
20 cm (7.9 inches)
32.4 cm (12 ¾ inches)

## Slide 3
The Products
（ステンレステープ） | (Stainless tape)
（ステンレスパンド） | (Stainless band)
（スチールテープ） | (Steel tape)
（スチールバンド） | (Steel band)
（シルバーテープ） | (Silver tape)
（タフテープ） | (Tough tape)
（スチロンテープ） | (Stylon tape)

## Slide 4
Measuring…
Nominal Conditions: 20 ºC, 2 kgf
Weight
Tension
Temperature
(10 kgf)

## Slide 5
T
L
Ct
Temperature - Ct
Ct = L · Kt · (T – T0) (result in mm)
L = measured length (m)
T = measured temperature (ºC)
T0 = nominal temperature (20 ºC)
Kt = tape temperature coefficient (mm/m·ºC)
Stainless Steel Kt
Steel Kt
Rear side, scales “L”, “T” and “± Ct mm”
Reading of 30 m at 15 ºC with steel tape?

## Slide 6
Cp
P0=2kg
L
F1
Tension - Cp
Front side, scales “L”, “F1”, “P0=2kg” and “+ Cp mm”
Reading of 50 m at 10 kgf with silver tape?
Cp = L · Kp · (P – P0) (result in mm)
L = measured length (m)
P = tension at measurement (kgf)
P0 = nominal tension (2 kgf or 10 kgf)
Kp = tape tension coefficient (mm/m·kgf)
Silver Tape

## Slide 7
Cs
Looseness - Cs
Stainless Band
L = distance between the support points (m)
P = tension (kgf)
w = weight per unit length of measuring tape (gf/m)
Front side, scales “L”, “F2”, “P” and “- Cs mm”
Reading of 50 m at 15 kgf with stainless band?

## Slide 8
P0=2kg
L
F3
Pn
(Tough Tape)
Positive Tension - Pn
Rear side, scales “L”, “F3” and “Pn kg”
Reading 30 m with tough tape?
L · Kp · (P – P0) =

## Slide 9
h
L2
Ci
Rear side, scales “L2”, “h” and “- Ci m”
Inclination - Ci
Reading of 30 m with height difference of 8 m?
Ci =

## Slide 10
Compensation Examples
Factor |  | Measurement | Correction | Result
Temperature | Ct | 30 m | 1.72 mm | 29.99828 m
Tension | Cp | 50 m | 7.6 mm | 50.0076 m
Looseness | Cs | 50 m | 18.1 mm | 49.9819 m
Positive Tension | Pn | 30 m | 7.1 kgf | 30 m
Inclination | Ci | 30 m | 1.05 m | 28.95 m
When the results are worth the effort?

## Slide 11
Scales Standardization
Front Side |  |  | Back Side | 
Scale Name | Scale Type |  | Scale Name | Scale Type
 |  |  | -Ci | AI2 (shifted)
 |  |  | L2 | A2
+Cp | A (shifted) |  | ±Ct | A (shifted)
Tension (P0=2kg)/(P0=10kg) | B* (shifted) |  | T (<20ºC/>20ºC) | BI*
P | 2/3BI |  | F3 | B
F1 - F2 | BI - 2/3BI |  | h.ℓ.δ | B
L | A |  | L | A
-Cs | A3 (shifted) |  | Pn (P0=2kg) | “A + D” (shifted)
 |  |  | Pn (P0=10kg) | “A + D” (shifted)
(*: with special numbering)

## Slide 12
Slide Rule Dating
Yamayo Webpage History Key Milestones
Slide Rule Possible Milestones
Possible end of slide rule commercialization
possible starting of slide rule usage
Possible starting of model slide rule design
Specimen first possible year of manufacture
Specimen last possible year of manufacture
Possible end of slide rule ordering to Fuji
1959: Approved factory for steel tape with JIS labeling
1966: Stylon tape commercialization
1968: Silver tape commercialization
1972: -
1988: Head office moved from Nihonbashi to Adachi
1989: Release of ready-to-use surveyor calculator
1990: Stylon, Million, Pro Series full model change
Slide Rule Manual Data
…”The above table was standardized in February 1972”…
…”Head Office … Nihonbashi Honcho”…

## Slide 13
Thank You!